## Slide 1: Control Systems (CS)
Lecture-1
Introduction to the Subject

## Slide 2: Outline
Course Outline
Recommended Books
Prerequisites of the subject
Basic Definitions
Types of Control Systems
Examples

## Slide 3
Classical Control
Modern Control
System Modelling
System Analysis
Transfer Function
Block Diagrams
Signal Flow Graphs
Time Domain Analysis
State Space Modelling
Bode Plots, Nyquist Plots, Nichol’s Chart
Transfer Function to State Space
State Space to Transfer Function
Solution of State Equations (state Transition Matrix)
Observability and Controllability
Eigenvalue Analysis
System Design
Compensation Techniques
PID Control
Frequency Domain Analysis
State Space Design Techniques
Root Locus

## Slide 4: Text Books
Modern Control Engineering, (5th Edition)
By: Katsuhiko Ogata.
(Prof Emeritus)
Mechanical Engineering
University of Minnesota
Control Systems Engineering, (6th Edition)
By: Norman S. Nise. (Professor Emeritus)
Electrical and Computer Engineering Department
at California State Polytechnic University

## Slide 5: Reference Books
Modern Control Systems, (12th Edition)
By: Richard C. Dorf and Robert H. Bishop.
2. Automatic Control Systems, (9th Edition)
By: Golnaraghi and B. C. Kuo.

## Slide 6: Prerequisites
For Classical Control Theory
  Differential Equations
  Laplace Transform
  Basic Physics
  Ordinary and Semi-logarithimic graph papers
For Modern Control theory above &
  Linear Algebra
  Matrices

## Slide 7: What is Control System?
A system Controlling the operation of another system.
A system that can regulate itself and another system.
A control System is a device, or set of devices to manage, command, direct or regulate the behaviour of other device(s) or system(s).

## Slide 8
Definitions
System – An interconnection of elements and devices for a desired purpose.
Control System – An interconnection of components forming a system configuration that will provide a desired response.
Process – The device, plant, or system under control. The input and output relationship represents the cause-and-effect relationship of the process.
Process
Output
Input

## Slide 9
Definitions
Controlled Variable– It is the quantity or condition that is measured and Controlled. Normally controlled variable is the output of the control system.
Manipulated Variable– It is the quantity of the condition that is varied by the controller so as to affect the value of controlled variable.
Control – Control means measuring the value of controlled variable of the system and applying the manipulated variable to the system to correct or limit the deviation of the measured value from a desired value.

## Slide 10
Definitions
Disturbances– A disturbance is a signal that tends to adversely affect the value of the system. It is an unwanted input of the system.
If a disturbance is generated within the system, it is called internal disturbance. While an external disturbance is generated outside the system.
Controller
Output
Or
Controlled Variable
Input
or
Set point
or
reference
Process
Manipulated Variable

## Slide 11: Types of Control System
Natural Control System
  Universe
  Human Body

## Slide 12: Types of Control System
Manmade Control System
  Aeroplanes
  Chemical Process

## Slide 13: Elevators
a. Early elevators were controlled by hand ropes or an elevator operator. Here, a rope is cut to demonstrate the safety brake, an innovation in early
elevators;
b. Modern Duo-lift elevators make their way up the Grande Arche in Paris, driven by one motor, with each car counterbalancing the other. Today, elevators are fully automatic, using control systems to regulate position and velocity.
Photos courtesy of United Technologies Otis Elevator.

## Slide 14: Elevator input and output

## Slide 15: Types of Control System
Manual Control Systems
  Room Temperature regulation Via Electric Fan
  Water Level Control
Automatic Control System
  Home Water Heating Systems (Geysers)
  Room Temperature regulation Via A.C
  Human Body Temperature Control

## Slide 16
Open-Loop Control Systems utilize a controller or control actuator to obtain the desired response.
Output has no effect on the control action.
In other words output is neither measured nor fed back.
Controller
Output
Input
Process
Examples:- Washing Machine, Toaster, Electric Fan, microwave oven, e.t.c
Types of Control System
Open-Loop Control Systems

## Slide 17
Open-Loop Control Systems
Types of Control System
Since in open loop control systems reference input is not compared with measured output, for each reference input there is fixed operating condition. Therefore, the accuracy of the system depends on calibration.
The performance of open loop system is severely affected by the presence of disturbances, or variation in operating/ environmental conditions.

## Slide 18
Closed-Loop Control Systems utilizes feedback to compare the actual output to the desired output response.
Examples:- Refrigerator, Electric Iron, Air conditioner
Types of Control System
Closed-Loop Control Systems
Controller
Output
Input
Process
Comparator
Measurement

## Slide 19
Multivariable Control System
Types of Control System
Controller
Outputs
Temp
Process
Comparator
Measurements
Humidity
Pressure

## Slide 20: Figure 1.6 Block diagrams of control systems: a. open-loop system; b. closed-loop system

## Slide 21
Feedback Control System
Types of Control System
A system that maintains a prescribed relationship between the output and some reference input by comparing them and using the difference (i.e. error) as a means of control is called a feedback control system.
Feedback can be positive or negative.
Controller
Output
Input
Process
Feedback
-
+
error

## Slide 22
Servo System
Types of Control System
A Servo System (or servomechanism) is a feedback control system in which the output is some mechanical position, velocity or acceleration.
Antenna Positioning System
Modular Servo System (MS150)

## Slide 23
Linear Vs Nonlinear Control System
Types of Control System
A Control System in which output varies linearly with the input is called a linear control system.
y(t)
u(t)
Process

## Slide 24
Linear Vs Nonlinear Control System
Types of Control System
When the input and output has nonlinear relationship the system is said to be nonlinear.

## Slide 25
Time invariant vs Time variant
Types of Control System
When the characteristics of the system do not depend upon time itself then the system is said to time invariant control system.
Time varying control system is a system in which one or more parameters vary with time.

## Slide 26
Continuous Data Vs Discrete Data System
Types of Control System
In continuous data control system all system variables are function of a continuous time t.
A discrete time control system involves one or more variables that are known only at discrete time intervals.
x(t)
t
X[n]
n

## Slide 27
Deterministic vs Stochastic Control System
Types of Control System
A control System is deterministic if the response to input is predictable and repeatable.
If not, the control system is a stochastic control system
y(t)
t
x(t)
t
z(t)
t

## Slide 28: Classification of Control Systems
Control Systems
Natural
Man-made
Manual
Automatic
Open-loop
Closed-loop
Non-linear
linear
Time variant
Time invariant
Non-linear
linear
Time variant
Time invariant
LTI Control Systems(Linear time invariant control systems)

## Slide 29
Examples of Control Systems
Water-level float regulator

## Slide 30
Examples of Control Systems

## Slide 31
Examples of Modern Control Systems

## Slide 32: Figure 1.11 The control system design process

## Slide 33: Table 1.1 Test waveforms used in control systems

## Slide 34: Figure P1.1 Potentiometer

## Slide 35
Q&A