## Slide 1: Control Systems (CS)
Lecture-2
Mathematical Modeling of Dynamic Systems
Note: I do not claim any originality in these lectures. The contents of this presentation are mostly taken from the book of Ogatta, Norman Nise, Bishop and B C. Kuo and various other internet sources.

## Slide 2: Outline
Introduction
Types of Models
Mathematical Modeling of
  Electrical Systems
  Electronic Systems
  Mechanical Systems
  Electromechanical Systems

## Slide 3: Types of Systems
Static System: If a system does not change with time, it is called a static system.
Dynamic System: If a system changes with time, it is called a dynamic system.

## Slide 4: Dynamic Systems
A system is said to be dynamic if its current output may depend on the past history as well as the present values of the input variables.
Mathematically,
Example: A moving mass
M
y
u
Model: Force=Mass x Acceleration

## Slide 5: Ways to Study a System
System
Experiment with a model of the System
Experiment with actual System
Physical Model
Mathematical Model
Analytical Solution
Simulation
Frequency Domain
Time Domain
Hybrid Domain

## Slide 6: Model
A model is a simplified representation or abstraction of reality.
Reality is generally too complex to copy exactly.
Much of the complexity is actually irrelevant in problem solving.

## Slide 7: What is Mathematical Model?
A set of mathematical equations (e.g., differential eqs.) that describes the input-output behavior of a system.
What is a model used for?
Simulation
Prediction/Forecasting
Prognostics/Diagnostics
Design/Performance Evaluation
Control System Design

## Slide 8
Mathematical Model  Mathematical modeling of any control system is the first and foremost task that a control engineer has to accomplish for design and analysis of any control engineering problem.  A mathematical model of a dynamic system is defined as a set of differential equations that represents the dynamics of the system accurately, or at least fairly well.  Note that a mathematical model is not unique to a given system. A system may be represented in many different ways and, therefore, may have many mathematical models, depending on one’s perspective. For example,  In optimal control problems, it is good to use state-space representations.  On the other hand, for the transient-response or frequency-response analysis of singleinput-single-output, linear, time-invariant systems, the transfer function representation may be more convenient than any other.

## Slide 9
 Once a mathematical model of a system is obtained, various analytical and computational techniques may be used for analysis and synthesis purposes. Because the systems under consideration are dynamic in nature, the equations are usually differential equations. If these equations can be linearized, then the Laplace transform may be utilized to simplify the method of solution. 3 Different Mathematical Models  Commonly used mathematical models are  Differential equation model (Time Domain).  Transfer function model (S-Domain).  State space model (Time Domain).  Use of the models depends on the application. For example, to find the transient or steady state response of SISO (Single Input Single Output) LTI (Linear Time Invariant) system transfer function model is useful. On the other hand for optimal control application state space model is useful.

## Slide 10: Black Box Model
When only input and output are known.
Internal dynamics are either too complex or unknown.
Easy to Model
Input
Output

## Slide 11: Grey Box Model
When input and output and some information about the internal dynamics of the system is known.
Easier than white box Modelling.
u(t)
y(t)
y[u(t), t]

## Slide 12: White Box Model
When input and output and internal dynamics of the system is known.
One should know have complete knowledge of the system to derive a white box model.
u(t)
y(t)

## Slide 13: Laplace Transform
Laplace Transforms: method for
solving differential equations,
converts differential equations
in time 𝑡 into algebraic
equations in complex variable 𝑠.

## Slide 14: Basic Elements of Electrical Systems
Component | Symbol | V-I Relation (Time Domain) | V-I Relation (Frequency Domain)
Resistor |  |  | 
Capacitor |  |  | 
Inductor |  |  | 

## Slide 15: Example#1
The two-port network shown in the following figure has vi(t) as the input voltage and vo(t) as the output voltage. Find the transfer function Vo(s)/Vi(s) of the network.
C
i(t)
vi( t)
vo(t)

## Slide 16: Example#1
Taking Laplace transform of both equations, considering initial conditions to zero.
Re-arrange both equations as:

## Slide 17: Example#1
Substitute I(s) in equation on left

## Slide 18: Example#1
The system has one pole at

## Slide 19: Example#2
Find the transfer function G(S) of the following two port network.
i(t)
vi(t)
vo(t)
L
C

## Slide 20: Example#2
Simplify network by replacing multiple components with their equivalent transform impedance.
I(s)
Vi(s)
Vo(s)
L
C
Z

## Slide 21: Transform Impedance (Resistor)
iR(t)
vR(t)
+
-
IR(S)
VR(S)
+
-
ZR = R
Transformation

## Slide 22: Transform Impedance (Inductor)
iL(t)
vL(t)
+
-
IL(S)
VL(S)
+
-
LiL(0)
ZL=LS

## Slide 23: Transform Impedance (Capacitor)
ic(t)
vc(t)
+
-
Ic(S)
Vc(S)
+
-
ZC(S)=1/CS

## Slide 24: Equivalent Transform Impedance (Series)
Consider following arrangement, find out equivalent transform impedance.
L
C
R

## Slide 25: Equivalent Transform Impedance (Parallel)
C
L
R

## Slide 26: Equivalent Transform Impedance
Find out equivalent transform impedance of following arrangement.
L2
L2
R2
R1

## Slide 27: Back to Example#2
I(s)
Vi(s)
Vo(s)
L
C
Z

## Slide 28: Example#2
I(s)
Vi(s)
Vo(s)
L
C
Z

## Slide 29: Modeling of Electronic Systems

## Slide 30: Operational Amplifiers

## Slide 31: Example#3
Find out the transfer function of the following circuit.

## Slide 32: Example#4
Find out the transfer function of the following circuit.
v1

## Slide 33: Example#5
Find out the transfer function of the following circuit.
v1

## Slide 34: Example#6
Find out the transfer function of the following circuit and draw the pole zero map.
10kΩ
100kΩ

## Slide 35: Modeling of Mechanical Systems
Part-I: Translational Mechanical System
Part-II: Rotational Mechanical System
Part-III: Mechanical Linkages

## Slide 36: Basic Types of Mechanical Systems
Translational
  Linear Motion
Rotational
  Rotational Motion

## Slide 37: Translational Mechanical Systems
Part-I

## Slide 38
Basic Elements of Translational Mechanical Systems
Translational Spring
i)
Translational Mass
ii)
Translational Damper
iii)

## Slide 39: Translational Spring
Translational Spring
i)
Circuit Symbols
A translational spring is a mechanical element that can be deformed by an external force such that the deformation is directly proportional to the force applied to it.
Translational Spring

## Slide 40: Translational Spring
If F is the applied force
Then is the deformation if
Or is the deformation.
The equation of motion is given as
Where is stiffness of spring expressed in N/m

## Slide 41
Translational Mass
Translational Mass
ii)
Translational Mass is an inertia element.
A mechanical system without mass does not exist.
If a force F is applied to a mass and it is displaced to x meters then the relation b/w force and displacements is given by Newton’s law.
M

## Slide 42
Translational Damper
Translational Damper
iii)
When the viscosity or drag is not negligible in a system, we often model them with the damping force.
All the materials exhibit the property of damping to some extent.
If damping in the system is not enough then extra elements (e.g. Dashpot) are added to increase damping.

## Slide 43
Common Uses of Dashpots
Door Stoppers
Vehicle Suspension
Bridge Suspension
Flyover Suspension

## Slide 44
Translational Damper
Where C is damping coefficient (N/ms-1).

## Slide 45: Example-7
Consider the following system (friction is negligible)
Free Body Diagram
M
Where and are forces applied by the spring and inertial force respectively.

## Slide 46: Example-7
Then the differential equation of the system is:
Taking the Laplace Transform of both sides and ignoring initial conditions we get
M

## Slide 47
The transfer function of the system is
if
Example-7

## Slide 48
The pole-zero map of the system is
Example-7

## Slide 49: Example-8
Consider the following system
Free Body Diagram
M

## Slide 50: Example-8
Differential equation of the system is:
Taking the Laplace Transform of both sides and ignoring
Initial conditions we get

## Slide 51: Example-8
if

## Slide 52: Example-9
Consider the following system
Mechanical Network
↑
M

## Slide 53: Example-9
Mechanical Network
↑
M
At node
At node

## Slide 54: Example-10
↑
M1
M2

## Slide 55: Rotational Mechanical Systems
Part-I

## Slide 56
Basic Elements of Rotational Mechanical Systems
Rotational Spring

## Slide 57
Basic Elements of Rotational Mechanical Systems
Rotational Damper

## Slide 58
Basic Elements of Rotational Mechanical Systems
Moment of Inertia

## Slide 59
Example-11
↑
J1
J2

## Slide 60
Example-12
↑
J1
J2

## Slide 61
Example-13

## Slide 62: Mechanical Linkages
Part-III

## Slide 63: Gear
Gear is a toothed machine part, such as a wheel or cylinder, that meshes with another toothed part to transmit motion or to change speed or direction.

## Slide 64: Fundamental Properties
The two gears turn in opposite directions: one clockwise and the other counterclockwise.
Two gears revolve at different speeds when number of teeth on each gear are different.

## Slide 65: Gear Ratio
You can calculate the gear ratio by using the number of teeth of the driver divided by the number of teeth of the follower.
We gear up when we increase velocity and decrease torque.
Ratio: 3:1
We gear down when we increase torque and reduce velocity.
Ratio: 1:3
Gear Ratio = # teeth input gear / # teeth output gear
= torque in / torque out = speed out / speed in
Follower
Driver

## Slide 66: Mathematical Modeling of Gear Trains
Gears increase or reduce angular velocity (while simultaneously decreasing or increasing torque, such that energy is conserved).
Number of Teeth of Driving Gear
Angular Movement of Driving Gear
Number of Teeth of Following Gear
Angular Movement of Following Gear
Energy of Driving Gear = Energy of Following Gear

## Slide 67: Mathematical Modeling of Gear Trains
In the system below, a torque, τa, is applied to gear 1 (with number of teeth N1, moment of inertia J1 and a rotational friction B1).
It, in turn, is connected to gear 2 (with number of teeth N2, moment of inertia J2 and a rotational friction B2).
The angle θ1 is defined positive clockwise, θ2 is defined positive clockwise. The torque acts in the direction of θ1.
Assume that TL is the load torque applied by the load connected to Gear-2.
B1
B2
N1
N2

## Slide 68: Mathematical Modeling of Gear Trains
For Gear-1
For Gear-2
Since
therefore
B1
B2
N1
N2
Eq (1)
Eq (2)
Eq (3)

## Slide 69: Mathematical Modeling of Gear Trains
Gear Ratio is calculated as
Put this value in eq (1)
Put T2 from eq (2)
Substitute θ2 from eq (3)
B1
B2
N1
N2

## Slide 70: Mathematical Modeling of Gear Trains
After simplification

## Slide 71: Mathematical Modeling of Gear Trains
For three gears connected together

## Slide 72: Modeling of Electromechanical Systems

## Slide 73
D.C Drives
Variable Voltage can be applied to the armature terminals of the DC motor .
Another method is to vary the flux per pole of the motor.
The first method involve adjusting the motor’s armature while the latter method involves adjusting the motor field. These methods are referred to as “armature control” and “field control.”

## Slide 74
Mechanical Subsystem
Input: voltage u
Output: Angular velocity 
Electrical Subsystem (loop method):
Example-14: Armature Controlled D.C Motor
u
ia
T
Ra
La
J

B
eb
Vf=constant

## Slide 75
Torque-Current:
Voltage-Speed:
Combing previous equations results in the following mathematical model:
Power Transformation:
Example-14: Armature Controlled D.C Motor
u
ia
T
Ra
La
J

B
eb
Vf=constant

## Slide 76
Taking Laplace transform of the system’s differential equations with zero initial conditions gives:
Eliminating Ia yields the input-output transfer function
Example-14: Armature Controlled D.C Motor

## Slide 77: Reduced Order Model
Assuming small inductance, La 0
Example-14: Armature Controlled D.C Motor

## Slide 78
If output of the D.C motor is angular position θ then we know
Which yields following transfer function
Example-14: Armature Controlled D.C Motor
u
ia
T
Ra
La
J
θ
B
eb
Vf=constant

## Slide 79
Applying KVL at field circuit
Example-15: Field Controlled D.C Motor
if
Tm
Rf
Lf
J
ω
B
Ra
La
ea
ef
Mechanical Subsystem

## Slide 80
Torque-Current:
Combing previous equations and taking Laplace transform (considering initial conditions to zero) results in the following mathematical model:
Power Transformation:
where Kf: torque constant
Example-15: Field Controlled D.C Motor

## Slide 81
If angular position θ is output of the motor
Eliminating If(S) yields
Example-15: Field Controlled D.C Motor
if
Tm
Rf
Lf
J
θ
B
Ra
La
ea
ef

## Slide 82
+
kp
-
JL
_
ia
eb
Ra
La
+
T
r
c
ea
_
+
e
_
+
N1
N2
BL
θ
if = Constant
JM BM
Example-16: Angular Position Control System

## Slide 83
Numerical Values for System constants
r = angular displacement of the reference input shaft
c = angular displacement of the output shaft
θ = angular displacement of the motor shaft
K1 = gain of the potentiometer shaft = 24/π
Kp = amplifier gain = 10
ea = armature voltage
eb = back emf
Ra = armature winding resistance = 0.2 Ω
La = armature winding inductance = negligible
ia = armature winding current
Kb = back emf constant = 5.5x10-2 volt-sec/rad
Kt = motor torque constant = 6x10-5 N-m/ampere
Jm = moment of inertia of the motor = 1x10-5 kg-m2
Bm=viscous-friction coefficients of the motor = negligible
JL = moment of inertia of the load = 4.4x10-3 kgm2
BL = viscous friction coefficient of the load = 4x10-2 N-m/rad/sec
n= gear ratio = N1/N2 = 1/10

## Slide 84
Example-16: Angular Position Control System
Transfer function of the armature controlled D.C motor with load connected to it is given by
Where

## Slide 85
Example-16: Angular Position Control System
Error is difference between reference input and out calculated and can be calculated as
Output of amplifier is
Merging eq (a) and eq (b) yields
Relation between angular position of motor and angular position of load is given as
or
E
(a)
(b)

## Slide 86
Example-16: Angular Position Control System
Final Closed loop transfer function of the system can now be written as

## Slide 87: End of Lecture-2
To download this lecture visit
http://imtiazhussainkalwar.weebly.com/